Lab 3 UART with Even Parity Bit
CSE 521 FPGA Design
Aaron Chamberlain, ID: 003392908

I Goals:
Serial communication, although by design is a very old communication protocol, is still widely used in many specific fields that are aided by computer design. Multi-meters, industrial tools, and even television broadcast equipment all continue to use the Serial communication method. Thus notably, it is a very common design paradigm that may need to be reproduced in a number of different chips and as a part of larger electrical designs. The goal of this lab is to learn the internal workings of the UART communication design by producing a working UART that uses at a minimum even or odd parity for error checking. In this design, many other smaller topics become important, such as syncing the bit transport stream to a clock so that all bits are signaled for a controlled amount of time.

II Design Process:
Given the obvious timing design constraints mentioned in the goals section above, the design will begin with a graph of the internal functional units. Given that we will be updating data registers over time, this design paradigm is most easily shown using an ASMD. Before we go about designing the mechanism for the creating our serial signals, we must first define the protocol communication standard. Most communication standards have very well defined signal bits and timing contraints, and the Serial protocol is one of them. So first, we will observe the packet standard as seen in (Figure 1).
Figure 1. The packet design and timing of Serial Communication

When in the idle state, we continue to simply send a stable logic level of one. When a packet is ready to be transmitted or received, the signal is switched to zero. In this way we recognize the negative edge of the signal and trigger the rest of the transmission circuit. When the start bit is detected, we begin a counter that is used to control the data sampling period. We count up to 7, and then begin to count from 0 to 15 again. In this way, each time the counter reaches 15, the data signal will be immediately in the middle of it’s transmission. This is a very effective way of compensating for skew, or the signaling latency present in the circuit.
Now we begin to reach the data section of the protocol. The data is an 8 bit representation of the value being sent, which means that we can only send values from 0 to 255 in decimal, but this is plenty sufficient if we handle the receipt of this data in software where combinations can be chained logically to derive more complex circuits. We simply take the value that we wish to transmit and send it bit by bit. As soon as the data has been completely sent, we signal a Logic level high to represent the stop bit, which will conveniently allow us to indefinitely remain in the idle state again until data transmission resumes.
Now that basics of the UART have been discussed without parity, we may introduce the subject of data parity and how it will be added to the previous circuit design. Data parity is one of many hardware methods of compensating for random signal degradation. This is sometimes in modern applications, but is extremely important in scientific or industrial applications. Data parity comes in two modes, odd or even parity and is a single additional bit added directly after the data. The parity bit represents the number of ones present in the data section of the transmission. As the transmitter is sending its signal, it calculates the parity that it will send. The receiving computer will also calculate the expected parity bit, and then compare the expected value against the actual value that was sent. If the values do not match, then we may assume that the data was incorrectly transmitted.
In even parity mode, the parity bit will be set to zero if an even number of ones is present in the data signal. In odd parity, the parity bit will be set to zero if an odd number of ones is present. Note that this bit is active low, so that if added immediately after data it will allow us to switch to the regular active high stop bit without changing the rest protocol design. So for example, if we transmit the value 85 in decimal, or 01010101, then in even parity mode, the parity bit will be set to zero. In an odd parity mode, this same signal will set the parity bit to one, because an odd number of ones is not present.
Finally, now that we discussed the details of the UART system, we can split the design of the transmission and receiving circuits into two smaller modules. The first of these modules is broken down in an ASMD below (see Figure 2).